## Slide 1: 3D Scanning Drone
Literature Review of Methods and Outline of Project Breakdown
Fabeha Raheel (2nd October, 2024)

## Slide 2: Definition of Requirements
Target Objects for 3D Modelling – Objects similar to the size of humans (at least 1.5 – 3 meters).
Resolution – Scanning resolution and level of detail has not been specified at this point in the project.
Scanning Range – The drone should be able to scan the object from a distance of 2-5 meters
Drone Type – Custom Pixhawk drone with ArduPilot firmware, high resolution gimbal camera and indoor positioning system
Operation – Autonomous
3D Modelling Approach – Photogrammetry

## Slide 3: Overview of Photogrammetry
Photogrammetry is a technique that involves taking multiple overlapping photographs of an object and processing them to create a detailed 3D model. The method calculates depth and dimensions by comparing multiple 2D images taken from different angles.
Specialized photogrammetry software are used to process the images, identify common points between them to stitch the photos together into a 3D model. A dense point cloud, mesh, or textured 3D model can also be generated.

## Slide 4: Overview of Photogrammetry
Photogrammetry uses Structure-from-Motion (SfM) process to identify common points across images and create a sparse point cloud.
The sparse point cloud is converted into a dense point clolud using Multi-View Stereo (MVS) techniques to create a mesh of the object.

## Slide 5: Project Breakdown
The project will involve 3 aspects:
  Building a Pixhawk-based ArduPilot drone capable of Autonomous Navigation in indoor environments.
  Integration of high-resolution gimbal camera for capturing high quality images for photogrammetric processing
  Development of a data capture system to capture good quality images with sufficient overlap
  Selecting a suitable, open-source photogrammetry software for 3D model reconstruction

## Slide 6: Autonomous Navigation in Indoor Environments
The drone should be able to circle around the object to scan it completely over 360 degrees.
Since the scanning process should be very consistent and stable, drone flight should be autonomous and not manual (because it is nearly impossible to fly a drone in perfect circle around the object in manual mode).
Problem: Pre-built autonomous navigation algorithms for drone rely on GPS data which cannot work in indoor environments.
Solution: We must develop autonomous navigation algorithms using an indoor positioning system like optical flow sensor (PX4 flow) or with Visual Inertial Odometry (Intel RealSense Tracking Camera).

## Slide 7: Integration of High-Resolution Gimbal Camera
For 3D scanning of objects, we need a high-resolution camera that can capture a stream of images continuously with sufficient overlap.
The resolution of the gimbal camera should be between 12 MP to 20 MP or higher to capture enough details for the objects.
The camera should have good low-light performance and a wide aperture as well as high dynamic range to capture details in both the bright and shadowy areas of the object..
The camera system needs to be integrated onto a drone platform with a gimbal to provide stability during drone flight.

## Slide 8: Development of Data Capture System
For photogrammetry, we need to develop a data capture system to capture the high-resolution images of the object with sufficient overlap (60-90%) from different angles around the object.
The object should be stationary at placed at a position with good lighting to ensure uniform image capture around all perspectives.
There should be an SD card with sufficient memory to store the large number of images required for 3D scanning.
The images should be stored in JPEG format for photogrammetric processing.

## Slide 9: Utilization of Open-source Photogrammetry Softwares for Mesh Generation
Some photogrammetry tools used for creating 3D models from drone-captured images include:
  Open Drone Map (ODM) Software – It is one of the most widely used open-source solutions for drone photogrammetry and works well for close-range models
  Meshroom – It provides a full photogrammetric pipeline, from feature detection to model texturing.
  COLMAP – It provides a general-purpose Structure-from-Motion (SfM) and Multi-View Stereo (MVS) pipeline with high accuracy. It is ideal for detailed, small to medium-sized objects.
  CloudCompare – It is more useful for cleaning and refining models after initial 3D reconstruction.